## Slide 1: Construction
Topic: Practical construction calculus
Route: Construction
Lesson 4: Using integration in construction
Notes: Image © Shutterstock/Freedomz

## Slide 2: In this lesson, we will:
use integration to determine the area under a curve in various construction situations;
measure and analyse total heat loss through a wall;
use integration to calculate the total amount of heat lost through a wall in a specific time period.
General competencies
English:
E2 Present information and ideas
E5 Synthesise information
Maths:
M2 Estimate, calculate and spot errors
M3 Proportion
M4 Use rules and formulae
M5 Process data
M8 Communicate using maths
Digital:
D3 Communicate and collaborate
Lesson 4: Using integration in construction
Introduction

## Slide 3: Using integration in construction
Lesson 4: Using integration in construction
As you watch the video, make a list of different ways integration is used in the construction industry.
Introduction
Notes: Use of calculus in the construction industry video: https://vimeo.com/1111914156/70b6d7679b

## Slide 4: Integration for the area under a curve
Lesson 4: Using integration in construction
Integration can be used to calculate the area under a curve, for example, when working out how many bricks to use under a curved roof.
Follow along using the Activity 1 Worked example worksheet.
Activity 1

## Slide 5: Worked example: Integration
Activity 1
Lesson 4: Using integration in construction
You are constructing a new roof for a factory similar to the shape shown in the image.
The proportions and roof line for an arch for the new building can be represented by the quadratic equation:
Calculate the area of brickwork that will be required to fill under the arch.

## Slide 6: Worked example: Integration
Activity 1
Lesson 4: Using integration in construction
The roof line is shown in the graph.
The area, A, under the curve between x = 0 m and x = 20 m is to be determined.
Write this as an integration calculation:

## Slide 7: Worked example: Integration
Activity 1
Lesson 4: Using integration in construction
Step 1: Integrate each term.
This is a definite integral: use square brackets and add the limits to the top and bottom bracket.
To integrate, add 1 to the power and divide by the new power.

## Slide 8: Worked example: Integration
Activity 1
Lesson 4: Using integration in construction
Step 2: Apply definite limits.

## Slide 9: Integration for the area under a curve: practice
Complete the practice questions on the worksheet.
Resources needed
L4 Activity 1 worksheet
L4 Activity 1 worksheet answers
Calculator
Lesson 4: Using integration in construction
Activity 1

## Slide 10: Analysing heat loss through a wall
Locate a brick/block cavity wall and estimate the age of its construction. Look up its age in the reference table on the worksheet and determine its U-value.
Measure the temperature on both the inside and outside of a wall every 20 minutes, at least 4–7 times.
Enter the data into a spreadsheet and calculate the temperature difference between inside and outside at each time interval.
Plot this data on a line graph and use the spreadsheet to generate a best fit line and display its equation.
Integrate the equation to find the total heat loss over the time period studied.
Resources needed
L4 Activity 2 worksheet
Thermometers
Excel spreadsheet
Lesson 4: Using integration in construction
Activity 2

## Slide 11: Analysing heat loss through a wall: worked example
Lesson 4: Using integration in construction
Activity 2
Temperature data was collected for heat loss through a wall.
The size of the wall was 8 m x 4 m
The wall had a U-value of 1.6 W/m2 K
Using the rate of heat loss formula , integrate the temperature data over a 1-hour period to find the total heat loss through the wall (H).

## Slide 12: Analysing heat loss through a wall: worked example
Lesson 4: Using integration in construction
Time t (minutes) | Inside temperature (°C) | Outside temperature (°C) | ∆T (°C)
0 | 26 | 11 | 15
10 | 26 | 12 | 14
20 | 26 | 14 | 12
30 | 26 | 16 | 11
40 | 26 | 18 | 8
50 | 26 | 19 | 7
60 | 26 | 21 | 5
Activity 2

## Slide 13: Analysing heat loss through a wall: worked example
Activity 2
Lesson 4: Using integration in construction

## Slide 14: Analysing heat loss through a wall: worked example
Plotting the data for time and temperature difference, we can see the points are roughly linear.
Activity 2
Lesson 4: Using integration in construction

## Slide 15: Analysing heat loss through a wall: worked example
Activity 2
Lesson 4: Using integration in construction
Step 1: Derive the linear equation for temperature difference over time.
We can find the equation of the line of best fit. It goes from about:
Where:
m is the gradient, the rate of change of temperature difference.
c is the intercept, the initial temperature difference.

## Slide 16: Analysing heat loss through a wall: worked example
Activity 2
Lesson 4: Using integration in construction
Find the gradient, m:
We will find the slope from the first point (0, 15) to the final point (60, 5)

## Slide 17: Analysing heat loss through a wall: worked example
Activity 2
Lesson 4: Using integration in construction
Find the intercept, c:
The intercept, c is the initial temperature difference at t = 0.
The initial temperature difference was = 15
So, c = 15

## Slide 18: Analysing heat loss through a wall: worked example
Activity 2
Lesson 4: Using integration in construction
So, the linear equation for the temperature difference is

## Slide 19: Analysing heat loss through a wall: worked example
Activity 2
Lesson 4: Using integration in construction
Step 2: Setting up the integral for heat loss.
We know that Q = UA , so we can find the total heat loss, H, by integrating the temperature difference over the time period from 0 to 60 minutes.

## Slide 20: Analysing heat loss through a wall: worked example
Activity 2
Lesson 4: Using integration in construction
Step 3: Integrate the function.

## Slide 21: Analysing heat loss through a wall: worked example
Activity 2
Lesson 4: Using integration in construction
Step 4: Evaluate the definite integral to find total heat loss.

## Slide 22: Analysing heat loss through a wall: worked example
Activity 2
Lesson 4: Using integration in construction
Convert to watt hours (by dividing by 60):
H = 30,720 watt minutes
H = watt hours
H = 512 watt hours

## Slide 23: Multiple-choice questions
In which scenario is integration most useful in construction?
calculating the area of a square room
estimating the total volume of earth to be removed from an excavation site
finding the length of a single straight beam
determining the number of bricks needed for a straight square wall
Plenary
Lesson 4: Using integration in construction

## Slide 24: Multiple-choice questions
B. estimating the total volume of earth to be removed from an excavation site
Answer
Lesson 4: Using integration in construction
Plenary
In which scenario is integration most useful in construction?
calculating the area of a square room
estimating the total volume of earth to be removed from an excavation site
finding the length of a single straight beam
determining the number of bricks needed for a straight square wall

## Slide 25: Multiple-choice questions
In which of the following situations would integration be most useful in construction?
calculating the number of roof tiles needed
estimating the total material required for a curved roof structure
determining the height of a single building column
finding the number of doors in a building
Lesson 4: Using integration in construction
Plenary

## Slide 26: Multiple-choice questions
B. estimating the total material required for a curved roof structure
Answer
Lesson 4: Using integration in construction
Plenary
In which of the following situations would integration be most useful in construction?
calculating the number of roof tiles needed
estimating the total material required for a curved roof structure
determining the height of a single building column
finding the number of doors in a building

## Slide 27: In this lesson, we have:
used integration to determine the area under a curve in various construction situations;
measured and analysed heat loss through a wall;
used integration to calculate the amount of heat lost through a wall in a specific time period.
Lesson 4: Using integration in construction
Plenary
General competencies
English:
E2 Present information and ideas
E5 Synthesise information
Maths:
M2 Estimate, calculate and spot errors
M3 Proportion
M4 Use rules and formulae
M5 Process data
M8 Communicate using maths
Digital:
D3 Communicate and collaborate

## Slide 28: Consolidation
Complete a report of your practical activity.
Practise some more calculations involving integration using the Consolidation Worksheet.
Then swap with a partner and use the worksheet answers to give your partner feedback.
Lesson 4: Using integration in construction
Consolidation
Resources needed
Consolidation Worksheet
Consolidation Worksheet answers