## Slide 1: Construction
Topic: Practical construction calculus
Lesson 1: Using the mid-ordinate rule in construction
Route: Construction
Notes: Image © Shutterstock/Freedomz

## Slide 2: In this lesson, we will:
explain the concept of cut and fill;
explain how an embankment is created and its purpose in construction;
estimate the area under a curve and apply this to a range of construction situations using the mid-ordinate rule.
Lesson 1: Using the mid-ordinate rule in construction
Introduction
General competencies
English:
E2 Present information and ideas
E5 Synthesise information
Maths:
M2 Estimate, calculate and spot errors
M3 Work with proportion
M4 Use rules and formulae
M5 Process data
Digital:
D3 Communicate and collaborate

## Slide 3: Construction techniques
What do you think is meant by the concept of cut and fill?
Why is it important in the construction industry?
Why is it an environmentally friendly construction method?
Introduction
Lesson 1: Using the mid-ordinate rule in construction
Notes: Image © Shutterstock/Hachi888

## Slide 4: Cut and fill
Cut and fill is used to modify the topography of a site by:
  cut: excavating material from one location;
  fill: using the material to fill another location.
Soil, rocks, gravel or other debris are moved to create a level surface or desired slope for various construction activities.
This method minimises the amount of material that needs to be transported to or from the site.
Lesson 1: Using the mid-ordinate rule in construction
Introduction

## Slide 5: Embankments
What do you think an embankment is?
Have you seen one before? If so, where?
Why are embankments important in road construction?
Lesson 1: Using the mid-ordinate rule in construction
Activity 1
Notes: Image © Shutterstock/syarifjmt

## Slide 6: What are embankments?
Lesson 1: Using the mid-ordinate rule in construction
What are embankments used for?
What materials are used to build embankments?
Why are profile boards used?
What are the main steps in the construction of an embankment?
Activity 1
Notes: Understanding embankments and their role in road construction video: https://vimeo.com/1111914267/5caffc9b4b

## Slide 7: Embankments
An embankment is a raised structure made of soil, rocks or other materials. They are:
used to support roads, railways or other infrastructure;
used to hold back water with the addition of an impermeable clay core (dam, levee);
carefully compacted in layers to ensure strength and stability.
Lesson 1: Using the mid-ordinate rule in construction
Activity 1
Notes: Image © Shutterstock/Johnny G Bowers

## Slide 8: Construction of an embankment
Preparation: Clear the area of vegetation and debris.
Layering and compacting: Add soil in layers, compacting each layer thoroughly before adding the next.
Using profile boards: Place profile boards along the length of the embankment to guide the shape and height.
Final shaping: Smooth the shape of the embankment to the desired dimensions.
Lesson 1: Using the mid-ordinate rule in construction
Activity 1

## Slide 9: Example of cut and fill
Activity 1
This image shows a proposed longitudinal elevation for a new road over an area of terrain.
Sketch the image and colour in the areas that you think should be ‘cut’ and those that should be ‘fill’.
Why is it important that the finished road is flat?
Lesson 1: Using the mid-ordinate rule in construction
Proposed formation level
Level of existing terrain

## Slide 10: Example of cut and fill
Activity 1
Lesson 1: Using the mid-ordinate rule in construction
Proposed formation level
Level of existing terrain

## Slide 11: Using the mid-ordinate rule
When building an embankment, it is important to determine how much material needs to be brought onto site.
The area of a road embankment cross-section forms an approximate curve when plotted on a graph.
In mathematics, the mid-ordinate rule is one technique that is used to estimate the area under a curve.
Activity 2
Lesson 1: Using the mid-ordinate rule in construction

## Slide 12: Case study: HS2
Miles of embankments are being created for HS2.
Calculating correct numbers ensures avoiding logistical challenges, such as creating extra material to be disposed of or areas left without enough material.
Construction workers need to determine which areas to borrow material from, using factors such as distance and type of materials to decide.
Mathematical techniques, such as the mid-ordinate rule, can be used to determine the volume of material that must be moved.
Activity 2
Lesson 1: Using the mid-ordinate rule in construction

## Slide 13: Mid-ordinate rule
The mid-ordinate rule is used to estimate the area under the curve.
An ordinate is the y-coordinate on a graph for a given x-coordinate.
The mid-ordinate is the ordinate at the interval midpoint.
Activity 2
Lesson 1: Using the mid-ordinate rule in construction
mid-ordinate, yi

## Slide 14: Mid-ordinate rule
Split the width of the curve into equal intervals.
Draw rectangles with:
    width = interval width (Δx)
    height = height of curve at interval midpoint (yi)
Approximate area under curve = sum of all rectangle areas
Activity 2
Lesson 1: Using the mid-ordinate rule in construction
mid-ordinate, yi

## Slide 15: Applying mid-ordinate rule to cut and fill
The cross-section of land can be drawn on a graph.
The proposed new level can also be drawn.
To apply the mid-ordinate rule to find the cut cross-section area and fill cross-section area, use rectangles drawn from the proposed new level.
The new level could be the same as the x-axis, but it may be in a different place, as in this diagram.
Activity 2
Lesson 1: Using the mid-ordinate rule in construction

## Slide 16: Worked example: Mid-ordinate rule
Activity 2
Lesson 1: Using the mid-ordinate rule in construction
Position (m) | Existing elevation (m) | Desired elevation (m)
0 | 2.5 | 2
2 | 3 | 2
4 | 2 | 2
6 | 1.5 | 2
8 | 1 | 2
10 | 1 | 2
You are tasked with designing a road that must pass through uneven terrain. To create a level road, you will need to cut soil from higher areas and fill soil to lower areas.
The cross-section of the terrain along a 10-metre stretch of road is shown in the table.
Use the mid-ordinate rule to calculate how much material will need to be brought onto site to create a suitable ground level to construct the road. The road is to be 8 metres wide.
Activity 2 worked example sheet can be used.

## Slide 17: Worked example: Mid-ordinate rule
Activity 2
Lesson 1: Using the mid-ordinate rule in construction
Step 1: Plot the existing and desired elevation on graph paper.
Position (m) | Existing elevation (m) | Desired elevation (m)
0 | 2.5 | 2
2 | 3 | 2
4 | 2 | 2
6 | 1.5 | 2
8 | 1 | 2
10 | 1 | 2

## Slide 18: Worked example: Mid-ordinate rule
Activity 2
Lesson 1: Using the mid-ordinate rule in construction
Step 2: Divide the base width of the cross-section into equal intervals.
The base width is 10 m.
Use 5 intervals.
10 ÷ 5 = 2 m
Add the intervals to the graph.

## Slide 19: Worked example: Mid-ordinate rule
Activity 2
Lesson 1: Using the mid-ordinate rule in construction
Step 2: Divide the base width of the cross-section into equal intervals.

## Slide 20: Worked example: Mid-ordinate rule
Activity 2
Lesson 1: Using the mid-ordinate rule in construction
Step 3: Determine the midpoint of each interval.
Midpoints
Interval 1: 2.75 m
Interval 2: 2.5 m
Interval 3: 1.75 m
Interval 4: 1.25 m
Interval 5: 1 m

## Slide 21: Worked example: Mid-ordinate rule
Activity 2
Lesson 1: Using the mid-ordinate rule in construction
Step 4: Measure the height of the cut or fill at each point.
Measure from the proposed level to the mid-ordinate:
Cut
Interval 1 = 0.75 m
Interval 2 = 0.5 m
Fill
Interval 3 = –0.25 m
Interval 4 = –0.75 m
Interval 5 = –1 m

## Slide 22: Worked example: Mid-ordinate rule
Activity 2
Lesson 1: Using the mid-ordinate rule in construction
Step 5: Calculate the area of each interval
Interval 1 = 0.75 m Area = 0.75 × 2 m = 1.5 m2
Interval 2 = 0.5 m Area = 0. 5 × 2 m = 1 m2
Interval 3 = –0.25 m Area = –0.25 × 2 m = –0.5 m2
Interval 4 = –0.75 m Area = –0.75 × 2 m = –1.5 m2
Interval 5 = –1 m Area = –1 × 2 m = –2 m2
Multiply the height by the interval width (2 m) to find the area of each interval.

## Slide 23: Worked example: Mid-ordinate rule
Activity 2
Lesson 1: Using the mid-ordinate rule in construction
Step 6: Add up the areas of all the intervals
Interval 1 Area = 0.75 × 2 m = 1.5 m2
Interval 2 Area = 0. 5 × 2 m = 1 m2
Interval 3 Area = –0.25 × 2 m = –0.5 m2
Interval 4 Area = –0.75 × 2 m = –1.5 m2
Interval 5 Area = –1 × 2 m = –2 m2
Total area = 1.5 + 1 – 0.5 – 1.5 – 2 = –1.5 m2
Find the sum of the areas to get the total area of the cross-section.
As the result is negative, this means the fill area is greater than the cut area.
The earthworks contractor will need to bring 1.5 m2 extra of earth per metre width of road.

## Slide 24: Worked example: Mid-ordinate rule
Activity 2
Lesson 1: Using the mid-ordinate rule in construction
Step 7: Calculate the volume of earth to be added or removed
Total area = –1.5 m2
    Volume = cross-section area × width of road
Find the sum of the areas to get the total area of the cross-section.
12 m3 of earth needs to be added.
= 1.5 m2 × 8 m
= 12 m3

## Slide 25: Using the mid-ordinate rule
Steps to using the mid-ordinate rule:
Step 1: Plot the ‘x’ and ‘y’ co-ordinates on graph paper.
Step 2: Divide the base width of the cross-section into equal intervals.
Step 3: Determine the midpoint of each interval.
Step 4: Measure the height of the cut or fill at each point.
Step 5: Calculate the area of each interval.
Step 6: Find the sum of the areas of all the intervals to estimate the area of the cross-section.
Step 7: Calculate the volume of earth to be added or removed.
Follow along using the Activity 2 Worked example.
Activity 2
Lesson 1: Using the mid-ordinate rule in construction

## Slide 26: Using the mid-ordinate rule
Activity 2
Lesson 1: Using the mid-ordinate rule in construction
A ≈ interval width × sum of mid-ordinates
mid-ordinate, yi

## Slide 27: Using the mid-ordinate rule: practice
Complete the practice questions on the worksheet.
Resources needed
L1 Activity 2 Worksheet
L1 Activity 2 Worksheet answers
Calculator
Graph paper
Activity 2
Lesson 1: Using the mid-ordinate rule in construction

## Slide 28: Reflection questions
Why is it important to divide the base width into equal segments when using the mid-ordinate rule?
How might the shape of the embankment affect the accuracy of your area calculation using the mid-ordinate rule?
In what other real-world situations may the mid-ordinate rule be useful?
Plenary
Lesson 1: Using the mid-ordinate rule in construction

## Slide 29: In this lesson, we have:
explained the concept of cut and fill;
explained how an embankment is created and its purpose in construction;
estimated the area under a curve and applied this to a range of construction situations using the mid-ordinate rule.
General competencies
English:
E2 Present information and ideas
E5 Synthesise information
Maths:
M2 Estimate, calculate and spot errors
M3 Work with proportion
M4 Use rules and formulae
M5 Process data
Digital:
D3 Communicate and collaborate
Plenary
Lesson 1: Using the mid-ordinate rule in construction

## Slide 30: Consolidation
Complete additional practice using the mid-ordinate rule to calculate the area of material needed for other road constructions.
Carry out some research into other situations where engineers would use the mid-ordinate rule and other roles in the construction industry that may use the mid-ordinate rule.
Resources needed
L1 Consolidation Worksheet
Calculator
Graph paper
Consolidation
Lesson 1: Using the mid-ordinate rule in construction