## Slide 1: Construction
Topic: Practical construction calculus
Route: Construction
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
Notes: Image © Shutterstock/Freedomz

## Slide 2: In this lesson, we will:
estimate the area under a curve and apply this to a range of construction situations using the trapezoidal rule;
estimate the area under a curve and apply this to a range of construction situations using Simpson’s rule;
compare the benefits and limitations of using the mid-ordinate, trapezoidal and Simpson’s rule in different situations.
General competencies
English:
E2 Present information and ideas
E5 Synthesise information
Maths:
M2 Estimate, calculate and spot errors
M3 Work with proportion
M4 Use rules and formulae
M5 Process data
Digital:
D3 Communicate and collaborate
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
Introduction

## Slide 3: Activity: Mid-ordinate rule steps
Rearrange the steps into the correct order.
Calculate the area of each interval.
Divide the base width of the cross-section into equal intervals.
Plot the ‘x’ and ‘y’ co-ordinates on graph paper.
Find the height at each midpoint.
Find the sum of all the interval areas.
Determine the midpoint of each interval.
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
Introduction

## Slide 4: Answer: Mid-ordinate rule steps
Step 1: Plot the ‘x’ and ‘y’ co-ordinates on graph paper.
Step 2: Divide the base width of the cross-section into equal intervals.
Step 3: Determine the midpoint of each interval.
Step 4: Find the height at each midpoint.
Step 5: Calculate the area of each interval.
Step 6: Find the sum of all the interval areas.
Introduction
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 5: Recall: What is meant by an embankment?
Embankments are structures built to support roads, railways or canals.
They provide a stable foundation and allow the construction of these routeways over obstacles such as valleys, rivers and uneven terrain.
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
Introduction
Notes: Image © Shutterstock/syarifjmt

## Slide 6: Recall: What is meant by cut and fill?
Cut and fill is used to modify the topography of a site by:
  cut: excavating material from one location;
  fill: using the material to fill another location.
Soil, rocks, gravel or other debris is moved to create a level surface or the desired slope for construction activities.
This method minimises the amount of material that needs to be transported to or from the site.
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
Introduction
Proposed formation level
Level of existing terrain

## Slide 7: The trapezoidal rule
The trapezoidal rule is another rule that can be used to estimate the area under a curve.
The curve is divided into equal intervals. Each interval of the cross-section is treated as a trapezium.
We use the ordinates at the endpoints of each interval. Remember: an ordinate is the y-coordinate on a graph for a given x-coordinate.
Activity 1
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
Notes: Image © Shutterstock/anutr tosirikul

## Slide 8: Area of a trapezium
Activity 1
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 9: Trapezoidal rule formula
Activity 1
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 10: Using the trapezoidal rule
Activity 1
Look at this graph of a cross-section of a road.
This curve has six ordinates (labelled y1 to y6).
The first ordinate y1 is 2.5 metres.
Find the ordinates:
y3
y4
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 11: Worked example: Trapezium rule
Activity 1
Position (m) | Existing elevation (m) | Desired elevation (m)
0 | 2.5 | 2
2 | 3 | 2
4 | 2 | 2
6 | 1.5 | 2
8 | 1 | 2
10 | 1 | 2
You are tasked with designing a road that must pass through uneven terrain. To create a level road, you will need to cut soil from higher areas and fill soil to lower areas.
The cross-section of the terrain along a 10-metre stretch of road is shown in the table.
Use the trapezium rule to calculate how much material will need to be brought onto site to create a suitable ground level to construct the road. The road is to be 8 m wide.
Activity 1 worked example sheet can be used.
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 12: Worked example: Trapezium rule
Activity 1
Step 1: Plot the curve on graph paper.
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
Position (m) | Existing elevation (m) | Desired elevation (m)
0 | 2.5 | 2
2 | 3 | 2
4 | 2 | 2
6 | 1.5 | 2
8 | 1 | 2
10 | 1 | 2

## Slide 13: Worked example: Trapezium rule
Activity 1
Step 2: Divide the base width of the cross-section into equal intervals.
The base width is 10 m.
Use 5 intervals.
10 ÷ 5 = 2 m
Add the intervals to the graph.
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 14: Worked example: Trapezium rule
Activity 1
Step 2: Divide the base width of the cross-section into equal intervals.
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 15: Worked example: Trapezium rule
Activity 1
Step 3: Label the points where you will measure the ordinates.
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 16: Worked example: Trapezium rule
Activity 1
Step 4: Measure the height of the cut or fill at each point.
Measure from the proposed level to the ordinate
y1 = 0.5 m
y2 = 1 m
y3 = 0 m
y4 = –0.5 m
y5 = –1 m
y6 = –1 m
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 17: Worked example: Trapezium rule
Activity 1
Step 5: Use the trapezium rule to calculate the area of cut and fill.
y1 = 0.5 m
y2 = 1 m
y3 = 0 m
y4 = –0.5 m
y5 = –1 m
y6 = –1 m
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 18: Using the trapezoidal rule
Activity 1
We can break down the trapezoidal rule into a number of steps.
Step 1: Plot the x- and y-coordinates on graph paper.
Step 2: Divide the base width of the cross-section into equal intervals.
Step 3: Label the points where you will measure the ordinates.
Step 4: Find the heights of each ordinate.
Step 5: Use the trapezoidal rule to calculate the area of cut and fill.
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 19: Using the trapezoidal rule: practice
Complete the practice questions on the worksheet.
Resources needed
L2 Activity 1 Worksheet
L2 Activity 1 Worksheet answers
Calculator
Graph paper
Activity 1
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
Notes: Image © Shutterstock/4045

## Slide 20: Reflection questions
Why is it important to divide the base width into intervals of equal width when using the trapezoidal rule?
How might the shape of the embankment affect the accuracy of your area calculation using the trapezoidal rule?
Can you think of any other real-world applications where the trapezoidal rule might be useful?
Activity 1
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 21: Parabolic curves
Activity 2
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
x
y
O

## Slide 22: Parabolic curves
Activity 2
Parabolic curves are seen in real life. For example:
the path of water from a fountain;
the shape of certain bridges;
the shape of a roof.
Why do you think parabolic curves are used in construction?
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
Notes: Image © Shutterstock/zdast

## Slide 23: Simpson’s rule
Simpson’s rule is a numerical method used to approximate the area under a curve.
It works by dividing the area into an even number of intervals and fitting a parabolic curve to each interval to approximate the curve.
Generally, Simpson’s rule is more accurate than the trapezoidal rule for estimating the area under a curve as it uses curves instead of straight lines to approximate the shape.
Activity 2
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 24: Simpson’s rule formula
Activity 2
Remember: Simpson’s rule can only be used with an odd number of ordinates. This means there needs to be an even number of intervals.
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 25: Worked example: Simpson’s rule
Activity 2
Lesson 2:Using the trapezoidal rule and Simpson’s rule in construction
Activity 2 worked example sheet can be used.
You are constructing a curved roof and wish to calculate the area of bricks that will be needed to complete the area under the roof.
The roof line of the building can be represented by a quadratic equation in the form:
Use Simpson’s rule to calculate the area under the roof.

## Slide 26: Worked example: Simpson’s rule
Activity 2
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
Step 1: Plot the curve on graph paper.

## Slide 27: Worked example: Simpson’s rule
Activity 2
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
Step 2: Divide the base width of the cross-section into equal intervals.
Simpson’s Rule requires an odd number of ordinates and, therefore, an even number of intervals.
The base width is 20 m
10 intervals gives 11 ordinates.
interval width = 20 ÷ 10 = 2 m
Add the intervals to the graph.

## Slide 28: Worked example: Simpson’s rule
Activity 2
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
Step 2: Divide the base width of the cross-section into equal intervals.

## Slide 29: Worked example: Simpson’s rule
Activity 2
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
Step 3: Label the points where you will measure the ordinates.

## Slide 30: Worked example: Simpson’s rule
Activity 2
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
Step 4: Find the height of each ordinate
y1 = 0 m
y2 = 7.5 m
y3 = 13 m
y4 = 17 m
y5 = 19 m
y6 = 20 m
y7 = 19 m
y8 = 17 m
y9 = 13 m
y10 = 7.5 m
y11 = 0 m

## Slide 31: Worked example: Simpson’s rule
Activity 2
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
Step 5: Calculate the area under the curve using Simpson’s rule.
y1 = 0 m
y2 = 7 m
y3 = 13 m
y4 = 17 m
y5 = 19 m
y6 = 20 m
y7 = 19 m
y8 = 17 m
y9 = 13 m
y10 = 7 m
y11 = 0 m

## Slide 32
Using Simpson’s rule
We can break down Simpson’s rule into a number of steps.
Step 1: Plot the curve on graph paper.
Step 2: Divide the base width of the cross-section into equal intervals.
Step 3: Label the points where you will measure the ordinates.
Step 4: Find the height of each ordinate.
Step 5: Use Simpson’s rule formula to estimate the area under the curve.
Activity 2
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 33: Simpson’s vs trapezoidal rule
Which rule do you think is likely to be most accurate for calculating the area under a curved roof?
Are there any situations where one rule would be better than the other?
Activity 2
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
Notes: Image © Shutterstock/Toniflap

## Slide 34: Using the Simpson’s rule: practice
Complete the practice questions on the worksheet.
Resources needed
L2 Activity 2 Worksheet
L2 Activity 2 Worksheet answers
Calculator
Graph paper
Activity 2
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 35: Comparing rules
Identify the rules to which each statements applies.
Plenary
 | Mid-ordinate rule | Trapezoidal rule | Simpson’s rule
Divide the base width into intervals of equal width. |  |  | 
Use mid-points to determine the ordinates. |  |  | 
Can be used with an even or odd number of ordinates. |  |  | 
Can be used with an odd number of intervals. |  |  | 
Areas of fill should be represented as negative values. |  |  | 
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction

## Slide 36: Comparing rules: answers
Plenary
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
 | Mid-ordinate rule | Trapezoidal rule | Simpson’s rule
Divide the base width into intervals of equal width. | ✔ | ✔ | ✔
Use mid-points to determine the ordinates. | ✔ |  | 
Can be used with an even or odd number of ordinates. | ✔ | ✔ | 
Can be used with an odd number of intervals. | ✔ | ✔ | 
Areas of fill should be represented as negative values. | ✔ | ✔ | ✔

## Slide 37: In this lesson, we have:
estimated the area under a curve and applied this to a range of construction situations using the trapezoidal rule;
estimated the area under a curve and applied this to a range of construction situations using Simpson’s rule;
compared the benefits and limitations of using the mid-ordinate, trapezoidal and Simpson’s rule in different situations.
Plenary
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction
General competencies
English:
E2 Present information and ideas
E5 Synthesise information
Maths:
M2 Estimate, calculate and spot errors
M3 Work with proportion
M4 Use rules and formulae
M5 Process data
Digital:
D3 Communicate and collaborate

## Slide 38: Consolidation
Study the case study and use the mid-ordinate rule, trapezoidal rule and Simpson’s rule to calculate the area of cut and fill for a road.
Compare the results you have obtained from the three methods, explaining any differences in the calculated areas and why those differences might have occurred.
Resources needed
L2 Consolidation Worksheet
L2 Consolidation answers 1
L2 Consolidation answers 2
Calculator
Graph paper
Consolidation
Lesson 2: Using the trapezoidal rule and Simpson’s rule in construction