## Slide 1: Engineering and Manufacturing: Core
Topic: Manipulating equations and calculus
Route: Engineering and Manufacturing
Resource 4: Calculus – Differentiation
Notes: Image © Shutterstock/Gorodenkoff

## Slide 2: In this resource, we will:
calculate the derivatives of polynomial functions using the power rule;
calculate rates of change using differentiation;
calculate maximum or minimum values in optimisation problems by setting the derivative to zero and using algebraic skills.
Skills
CSE (Communicate and present outcomes and evidence)
General competencies
English:
EC1 Convey technical information to different audiences
Maths:
MC2 Estimating, calculating and error spotting
Introduction
Resource 4: Calculus – Differentiation

## Slide 3: Calculus – Differentiation
Introduction
  Calculus is fundamental throughout engineering and manufacturing.
  It is a branch of maths that consists of two key parts:
  differential calculus;
  integral calculus.
Differential calculus helps to understand the rate of change of one quantity in relation to another.
Resource 4: Calculus – Differentiation

## Slide 4: Differentiation in industry
Differentiation is essential in industry, including when:
calculating velocity and acceleration of moving objects;
finding operating speeds that minimise costs;
optimising designs for manufacturing;
identifying when normal operating parameters of systems are being exceeded, and by how much.
Introduction
Resource 4: Calculus – Differentiation
Notes: Image © Shutterstock/Gorodenkoff

## Slide 5: Polynomials
A polynomial is a mathematical expression made of terms with variables raised to a whole-number power or index.
Polynomials are common in engineering modelling.
is a function of
is a coefficient
is a variable
Terms are added or subtracted: , and 9 are terms
is a constant
has coefficient 1, even though it is not written
3 is a power or index
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 6: Differentiation of polynomials
The power rule: for each term
multiply the coefficient by the power
reduce the power by 1
variables without coefficients shown have coefficient 1;
has power 1 and differentiates to its constant coefficient;
constants differentiate to 0.
Keep in mind
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 7: Differentiation practice
Find :
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 8: Differentiation practice: Answers
Find :
Find the rate of change at by substituting:
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 9: Differentiation practice: Answers
Find :
Find the rate of change at by substituting:
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 10: Rates of change
Imagine the position of an object is describing a function of time
The rate of change of position is called velocity :
and are related by differentiation.
also written as
Differentiation gives the rate of change of the function for any .
Acceleration is the rate of change of velocity:
For this example because the velocity is constant.
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 11: Optimisation
Differentiation is useful for finding the minimum or maximum of a function.
At a minimum or maximum, the gradient (or rate of change) is zero.
That is, a minimum or maximum occurs where the derivative equals zero.
Imagine at the top of a hill or bottom of a valley, even if just for a small spot, the gradient goes neither up nor down.
The second derivative tells us whether it is a maximum or minimum.
Click to play the animation above
Resource 4: Calculus – Differentiation
Recap and Worked examples
Notes: Made with GeoGebra®

## Slide 12: Maximum or minimum
Find the critical points,
Find at the critical points
To find the maximum and minimum of
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 13: Maximum or minimum: Answers
Find the critical points,
Find at the critical points
To find the maximum and minimum of
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 14: Maximum or minimum: Answers
Find at the critical points
To find the maximum and minimum of
positive means is a minimum
negative means is a maximum
Resource 4: Calculus – Differentiation
Recap and Worked examples
Find the critical points,

## Slide 15: Worked example 1: Box size optimisation
Find the function for the volume of a box in terms of with the given dimensions, then find the derivative of the expression.
Use the formula:
with the variable dimensions:
Derive the volume function.
Expand the expression to form a cubic polynomial.
Find the derivative .
Resource 4: Calculus – Differentiation
Recap and Worked examples
Notes: Image © Shutterstock/Richard Peterson

## Slide 16: Worked example 1: Box size optimisation
Step 1: Derive the volume function.
Substitute the values into the formula (in terms of ).
This gives the volume in terms of .
Two or more sets of brackets written next to each other mean they are multiplied together.
Resource 4: Calculus – Differentiation
Recap and Worked examples
Notes: Image © Shutterstock/Richard Peterson

## Slide 17: Worked example 1: Box size optimisation
Step 2: Expand the brackets.
Multiply by everything in the second brackets.
Multiply by everything in the second brackets.
Then combine the results
and simplify
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 18: Worked example 1: Box size optimisation
Step 3: Continue expanding the bracket.
Multiply all terms in the first brackets by .
So, the volume of the box is represented by the polynomial
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 19: Worked example 1: Box size optimisation
Step 4: Differentiate term by term.
When differentiating polynomials, multiply the coefficient by the index, then reduce the index by one.
can be written as . When differentiated, the index reduces to 0, so the result is .
Anything to the power of 0 is 1, so the derivative of is .
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 20: Worked example 2: Finding the optimal point
The cost () of running a specific manufacturing process depends on the operating speed () and is given by:
Find the operating speed () that minimises the cost.
Express the parameter to be optimised as a function of the variable you can change. Here cost is a function of speed:
Calculate the first derivative, .
Find critical points. Set the derivative equal to zero , and solve for .
Confirm maximum or minimum with the second derivative test: Check whether second derivative, , is negative or positive at the critical points.
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 21: Worked example 2: Finding the optimal point
Step 1: Differentiate the cost function.
Differentiate term by term.
When you differentiate a number (a constant), the result is always 0.
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 22: Worked example 2: Finding the optimal point
Step 2: Set the derivate equal to zero to find the minimum point.
So, we need to solve forto make .
To find critical points: Set the derivative equal to zero and solve.
If the second derivative is negative, the critical point will be a maximum.
If the second derivative is positive, the critical point will be a minimum.
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 23: Worked example 2: Finding the optimal point
Step 3: Solve for .
To get on its own:
Add 24 to both sides of the equation
Divide both sides of the equation by 4
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 24: Worked example 2: Finding the optimal point
Step 4: Calculate the minimum cost.
Substitute back into .
So, the minimum cost is £78.
Remember to use the correct order of operations when calculating so brackets first .
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 25: Worked example 2: Finding the optimal point
Step 5: Show that is a minimum.
Find the second derivative of by taking the derivative of .
which is positive, so is indeed a minimum.
To find critical points: Set the derivative equal to zero and solve.
If the second derivative is negative, the critical point will be a maximum.
If the second derivative is positive, the critical point will be a minimum.
Resource 4: Calculus – Differentiation
Recap and Worked examples

## Slide 26: Activity 1 – Box optimisation
You are a Design Engineer tasked with reducing material waste and increasing the efficiency of a key component.
In this example, the company is producing a protective casing for a new electronic control unit. Standard aluminium stock sheets are supplied at 30 cm × 20 cm.
You must use differentiation to find the dimensions that result in the maximum possible volume for an open-top box made from a 30 cm × 20 cm sheet of material with box height .
20 cm
30 cm
Resource 4: Calculus – Differentiation
Activity 1