## Slide 1: Engineering and Manufacturing: Core
Topic: Manipulating equations and calculus
Route: Engineering and Manufacturing
Resource 2: Formulae and rearrangement
Notes: Image © Shutterstock/Gorodenkoff

## Slide 2: In this resource, we will:
calculate values by substituting into engineering formulae
calculate any given variable by rearranging formulae
calculate torque, pressure (Pascal's Law) and electrical quantities (Ohm's Law formulae).
Skills
CSC (Develop response/s using key skills and processes)
General competencies
English:
EC5 Synthesise information
Maths:
MC4 Using rules and formulae
MC7 Interpreting and representing with mathematical diagrams
Digital:
DC4 Process and analyse numerical data
Introduction
Resource 2: Formulae and rearrangement

## Slide 3: Formulae as recipes
We are making final velocity, .
It’s the subject.
The ingredients for are variables.
is initial speed.
is acceleration.
is time.
The formula says how to combine them.
Introduction
Resource 2: Formulae and rearrangement
Notes: Image © Shutterstock/JOAT

## Slide 4: Orange Racing by JMH video – formulae in industry
Introduction
Resource 2: Formulae and rearrangement
Notes: Formulae and rearrangement in industry video: https://vimeo.com/1199780576/490c675b4c

## Slide 5: Substitution in formulae
Formulae show the relationship between different physical quantities.
For example, to convert ºC to K:
where
is the temperature in kelvin
ºCis the temperature in degrees Celsius.
What is 22 ºC in kelvin?
Recap and Worked examples
Resource 2: Formulae and rearrangement

## Slide 6: Substitution in formulae
Formulae show the relationship between different physical quantities.
For example, to convert ºC to K:
where
is the temperature in kelvin
ºCis the temperature in degrees Celsius.
What is 22 ºC in kelvin?
Substitute 22 for ºC:
Simplify:
Don’t forget the units!
Recap and Worked examples
Resource 2: Formulae and rearrangement

## Slide 7: Substitution in area of a circle
The area of a circle is:
where
is the area
is a constant,
is the radius.
We can find the area using the radius and .
Find the area of a circle with radius 3 cm.
Recap and Worked examples
Resource 2: Formulae and rearrangement

## Slide 8: Substitution in area of a circle
Find the area of a circle with radius 3 cm.
Substitute :
The units are squared when the radius is.
The area of a circle is:
where
is the area
is a constant,
is the radius.
We can find the area using the radius and .
Recap and Worked examples
Resource 2: Formulae and rearrangement

## Slide 9: Worked example 1: Using formulae
Resource 2: Formulae and rearrangement
The pitch control arm has a pivot radius of 1.2 m.
The scale model exerts a weight (force) of 2000 N at this distance.
Calculate the required torque in Nm.
Use the formula:
where
Recap and Worked examples

## Slide 10: Worked example 1: Using formulae
The pitch control arm has a pivot radius of 1.2 m.
The scale model exerts a weight (force) of 2000 N at this distance.
Calculate the required torque in Nm.
Step 1: Write out the calculation formula:
Resource 2: Formulae and rearrangement
This means that
Recap and Worked examples

## Slide 11: Worked example 1: Using formulae
The pitch control arm has a pivot radius of 1.2 m.
The scale model exerts a weight (force) of 2000 N at this distance.
Calculate the required torque in Nm.
Step 2: Fill in the known values for and :
Resource 2: Formulae and rearrangement
Remember to add units with your values.
Recap and Worked examples

## Slide 12: Worked example 1: Using formulae
The pitch control arm has a pivot radius of 1.2 m.
The scale model exerts a weight (force) of 2000 N at this distance.
Calculate the required torque in Nm.
Step 3: Calculate the final value:
Resource 2: Formulae and rearrangement
Many quantities have a composite unit, a unit made up of the units of quantities from which it has been calculated, like in this example.
Recap and Worked examples

## Slide 13: Rearranging formulae
How can we convert degrees kelvin to Celcius?
Rearrange the formula to be ºC by itself.
Subtract 273.15 from both sides.
What is 300 K in ºC?
º
Substitute 300 for K:
º
Simplify:
º
Don’t forget the units!
Recap and Worked examples
Resource 2: Formulae and rearrangement

## Slide 14: Rearranging area of a circle
What is the radius of a circle with area 25 cm2?
must be isolated on one side of the equation by using inverse operations and then found by substituting the area:
Divide both sides by pi
Square root both sides:
Radius cannot be negative, so take the positive value.
Recap and Worked examples
Resource 2: Formulae and rearrangement

## Slide 15: Worked example 2: Rearranging formulae
Resource 2: Formulae and rearrangement
The pitch control arm requires a maximum torque of 3000 Nm for safety.
The pivot radius is 1.5 m.
Calculate the maximum force that can be applied at this distance.
Use the formula:
where
Recap and Worked examples

## Slide 16: Worked example 2: Rearranging formulae
Resource 2: Formulae and rearrangement
The pitch control arm requires a maximum torque of 3000 Nm for safety.
The pivot radius is 1.5 m.
Calculate the maximum force that can be applied at this distance.
Step 1: Write out the calculation formula:
This means that
Recap and Worked examples

## Slide 17: Worked example 2: Rearranging formulae
Resource 2: Formulae and rearrangement
The pitch control arm requires a maximum torque of 3000 Nm for safety.
The pivot radius is 1.5 m.
Calculate the maximum force that can be applied at this distance.
Step 2: Rearrange the formula to make the unknown (force) the subject:
Divide both sides by .
The ’s on the righthand side cancel.
Always rearrange a formula before adding any values.
Recap and Worked examples

## Slide 18: Worked example 2: Rearranging formulae
Resource 2: Formulae and rearrangement
The pitch control arm requires a maximum torque of 3000 Nm for safety.
The pivot radius is 1.5 m.
Calculate the maximum force that can be applied at this distance.
Step 3: Fill in known values for and :
Recap and Worked examples

## Slide 19: Worked example 2: Rearranging formulae
Resource 2: Formulae and rearrangement
The pitch control arm requires a maximum torque of 3000 Nm for safety.
The pivot radius is 1.5 m.
Calculate the maximum force that can be applied at this distance.
Step 4: Calculate the final value:
Recap and Worked examples