## Slide 1: Engineering and Manufacturing: Core
Topic: Manipulating equations and calculus
Route: Engineering and Manufacturing
Resource 3: Mechanical calculations
Notes: Image © Shutterstock/Gorodenkoff

## Slide 2: In this resource, we will:
calculate speed ratio, torque, power and belt speed for a mechanical system;
explain the relationship between input power, output power and efficiency;
analyse an industry-relevant belt system scenario.
Skills
CSC (Develop response/s using key skills and processes)
CSE (Communicate and present outcomes and evidence)
General competencies
English:
EC2 Present information and ideas
Maths:
MC3 Working with proportion
MC10 Optimising work processes
MC8 Communicating using mathematics
Digital:
DC4 Process and analyse numerical data
Introduction
Resource 3: Mechanical calculations

## Slide 3: Conveyor belt systems
Conveyor belts are fundamental to the smooth running of many industries including factories, airports and mines.
Their purpose is to transport materials quickly and efficiently from one place to another.
Resource 3: Mechanical calculations
Introduction
Notes: Image © Shutterstock/Gorodenkoff

## Slide 4: Conveyor belt systems
Consist of a looped belt stretching over two (or more) wheels.
One wheel (the drive pulley) is powered by a motor. When it turns, it pulls the belt along.
The belt becomes a moving floor. Items placed on the top travel along the belt.
Idler rollers (non-powered) underneath support the belt and load.
Once items reach the end, they drop off. The belt loops back underneath, ready for the next batch. It’s a continuous cycle.
Resource 3: Mechanical calculations
Introduction
Notes: Image © Shutterstock/AIexVector

## Slide 5: Conveyor belt systems
Conveyor belts:
make it easy to move heavy, bulky or awkward items quickly and efficiently;
save time;
reduce the need for labour;
are versatile – they can go straight, up an incline, or around a curve; this allows them to move materials across floors, up ramps and around corners.
Resource 3: Mechanical calculations
Introduction
Notes: Image © Shutterstock/Gorodenkoff

## Slide 6: Activity 1
You are a Commissioning Engineer at a manufacturing plant where a new conveyor system has just been installed.
The contractor who installed the system provided a data sheet of theoretical performance values, but they used mixed units.
Your task is to review and confirm the key operational parameters – speed, torque and power – to ensure the system runs safely and efficiently before final handover.
Recap and Worked examples
Resource 3: Mechanical calculations

## Slide 7: Circles
Radius is the distance from the centre of the circle to the edge.
Diameter is the distance of the line passing through the centre of the circle. It is double the radius.
Circumference is the distance around the circle.
is a constant that relates circumference and radius.
Resource 3: Mechanical calculations
Recap and Worked examples

## Slide 8: Revolutions and rotational speed
The roller of a conveyor belt can be modelled as a circle rotating about its centre.
When a circle makes one complete rotation, this is called a revolution.
The rate at which the circle rotates is called its angular speed (or rotational speed). This can be measured in revolutions per minute (rpm).
Resource 3: Mechanical calculations
Recap and Worked examples
belt

## Slide 9: Revolutions to distance example 1
A roller of a conveyor belt has radius 5 cm, and it is rotating at 20 rpm.
How far does the belt travel in one minute?
Resource 3: Mechanical calculations
Recap and Worked examples
belt

## Slide 10: Revolutions to distance example 1: Answer
A roller of a conveyor belt has radius 5 cm, and it is rotating at 20 rpm.
How far does the belt travel in one minute?
One rotation moves the belt one circumference:
In one minute, the belt rotates 20 times, so:
Resource 3: Mechanical calculations
Recap and Worked examples
belt

## Slide 11: Revolutions to distance example 2
A roller of a conveyor belt has radius 5 cm, and it is rotating at 20 rpm.
How far does the belt travel in one minute?
Since the belt travels 6.28 m in 1 minute, its speed is 6.28 m/min. Convert this speed to m/s.
Resource 3: Mechanical calculations
Recap and Worked examples
belt

## Slide 12: Revolutions to distance example 2: Answer
A roller of a conveyor belt has radius 5 cm, and it is rotating at 20 rpm.
How far does the belt travel in one minute?
Since the belt travels 6.28 m in 1 minute, its speed is 6.28 m/min. Convert this speed to m/s.
belt
Resource 3: Mechanical calculations
Recap and Worked examples

## Slide 13: Belt speed formula
The previous example calculated belt speed by calculating circumference and multiplying by rpm, then converting to m/s by dividing by 60.
The formula for belt speed in m/s is:
where is speed, is circumference, is radius, is diameter, is angular speed in rpm.
Resource 3: Mechanical calculations
Recap and Worked examples
belt

## Slide 14: Speed ratio
Conveyor belts are not powered by their rollers, but instead by a motor with drive pulleys. The drive pulley is also modelled as a rotating circle.
The drive pulley and rollers are connected by the belt, so the smaller rollers must rotate faster to keep up with the motor:
Resource 3: Mechanical calculations
Recap and Worked examples

## Slide 15: SI units for angular speed
Angular speed is often given in revolutions per minute (rpm). But the SI unit is radians per second (rad/s).
1 revolution = radians, so:
So, to convert from rpm to rad/s, multiply by:
Resource 3: Mechanical calculations
Recap and Worked examples

## Slide 16: Motors, torque and power
Electric motors are commonly specified by power or rated speed.
Torque and power are related by the angular speed:
where is power, is angular speed in radians per second, is rpm, is torque.
Resource 3: Mechanical calculations
Recap and Worked examples
Notes: Image © Shutterstock/Vladimir Nenezic

## Slide 17: Motors example
A motor is driving a conveyor belt. Calculate the revolutions per minute required to provide 2000 W of power.
Resource 3: Mechanical calculations
Recap and Worked examples

## Slide 18: Motors example: Answer
A motor is driving a conveyor belt. Calculate the revolutions per minute required to provide 2000 W of power.
Rearrange the power equation for :
Substitute values and calculate:
Resource 3: Mechanical calculations
Recap and Worked examples

## Slide 19: Worked example: Calculating output power
Calculate the output power () in kilowatts () if the input power () to the belt system is 10 kW and the system operates at an efficiency () of 85%. (Efficiency measures how much of the input power is converted into useful output power.)
Use the formula:
where:
is efficiency
is output power
is input power.
Resource 3: Mechanical calculations
Recap and Worked examples

## Slide 20: Worked example: Calculating output power
This means that…
efficiency = output power ÷ input power
Calculate the output power () in kilowatts () if the input power () to the belt system is 10 kW and the system operates at an efficiency () of 85%.
Step 1: Write out the formula.
This means that …
efficiency = output power ÷ input power
Resource 3: Mechanical calculations
Recap and Worked examples

## Slide 21: Worked example: Calculating output power
This means that…
efficiency = output power ÷ input power
Calculate the output power () in kilowatts () if the input power () to the belt system is 10 kW and the system operates at an efficiency () of 85%.
Step 2: Rearrange the formula to make output power the subject.
Multiply both sides by
Cancel
Reverse equation
Always rearrange a formula before substituting any values.
Resource 3: Mechanical calculations
Recap and Worked examples

## Slide 22: Worked example: Calculating output power
This means that…
efficiency = output power ÷ input power
Calculate the output power () in kilowatts () if the input power () to the belt system is 10 kW and the system operates at an efficiency () of 85%.
Step 3: Convert the efficiency percentage to a decimal.
To convert a percentage to a decimal divide by 100.
Resource 3: Mechanical calculations
Recap and Worked examples

## Slide 23: Worked example: Calculating output power
This means that…
efficiency = output power ÷ input power
Calculate the output power () in kilowatts () if the input power () to the belt system is 10 kW and the system operates at an efficiency () of 85%.
Step 4: Fill in the known values and calculate.
Remember to include units on the final answer.
Resource 3: Mechanical calculations
Recap and Worked examples