## Slide 1: Building Services Engineering
Topic: Practical mathematics
Route: Construction
Resource 3: Key mathematical electricity principles
Notes: Image © Shutterstock/Gorodenkoff

## Slide 2: Key mathematical electricity principles for construction
Resource 3: Key mathematical electrical principles
Video
Notes: Key mathematical electricity principles for construction video: https://vimeo.com/1206421590/4643d373fd

## Slide 3: In this resource, we will:
Explain key mathematical electricity science principles and their importance
Describe and recall the rules of electrical circuits
Calculate with and recall Ohm’s law (V = IR) for a variety of different scenarios
Complete calculations involving key formulae
Calculate problems involving electrical power and its relationship with voltage
Calculate problems involving electrical power dissipation
Describe the basics of transformers
Calculate problems involving step-up and step-down transformers
General competencies:
MC4 Using rules and formulae
MC5 Processing data
MC7 Interpreting and representing with mathematical diagrams
MC8 Communicating using mathematics
Resource 3: Key mathematical electrical principles
Introduction

## Slide 4: Electrical quantities
A circuit is a closed loop where electricity can flow.
Key circuit quantities:
Voltage: The push that makes electricity move around the circuit. You may see the terms potential difference or electromotive force in different contexts.
Current: The flow of electric charge in the circuit.
Resistance: How much a component resists the flow of current.
Can you match the SI units to the quantity?
Ω, ohms
A, amperes
V, volts
Resource 3: Key mathematical electrical principles
Series and parallel circuits

## Slide 5: Basic circuit components
Wire
Battery
Switch
Resistor
+
–
+
–
Resource 3: Key mathematical electrical principles
Series and parallel circuits

## Slide 6: Parallel and series circuits
Before learning how to do calculations for electrical circuits, it is important to understand parallel and series circuits.
The relationship between voltage, current, resistance and power depends on the circuit arrangement.
Resource 3: Key mathematical electrical principles
Series and parallel circuits
Notes: Image © Shutterstock/Jesus Linares

## Slide 7: Parallel circuits
The battery and resistors are wired in parallel.
The voltage is the same across all parallel components: V = V 1 =V2
The current from the battery is split between the resistors: I = I1 + I2
The equivalent resistance of the circuit is less than either of the individual resistors and is related by: .
Resource 3: Key mathematical electrical principles
Socket outlets are wired in parallel.
If you plug a drill into Socket A, it does not affect the voltage at Socket B.
+
–
V
V1
V2
I
I1
I2
R1
R2
Series and parallel circuits

## Slide 8: Series circuits
Resource 3: Key mathematical electrical principles
+
–
V
V1
V2
R1
R2
I
The battery and resistors are wired in series.
The current flows through all of the components: I
The voltage from the battery is divided between the resistors: V =V1 +V2
The total resistance is the sum of the individual resistances: Rtotal = R1 + R2
If one component fails, electricity does not flow.
This is why we rarely use series for power, but it is useful for safety interlocks.
Series and parallel circuits

## Slide 9: Ohm’s Law
An important formula used in electricity principles is Ohm's Law.
This formula describes the relationship between voltage, current and resistance.
On site, we use a multimeter set to:
Ω to find Resistance (Continuity Check).
V to check if a circuit is Live (Safe Isolation).
Rearrange Ohm’s Law as:
Practice
Resource 3: Key mathematical electrical principles
Ohm’s Law

## Slide 10: Ohm’s Law in a parallel circuit
Consider the diagram. If a total current of 9 A is required, what is the required voltage?
Hint: first find the equivalent resistance of the circuit.
+
–
V
I
R1 = 6 Ω
R2 = 3 Ω
Resource 3: Key mathematical electrical principles
Ohm’s Law

## Slide 11: Ohm’s Law in a parallel circuit: Answer
Consider the diagram. If a total current of 9 A is required, what is the required voltage?
First find the equivalent resistance:
, so
Use Ohm’s Law to calculate the voltage:
+
–
V
I
R1 = 6 Ω
R2 = 3 Ω
Resource 3: Key mathematical electrical principles
Ohm’s Law

## Slide 12: Ohm’s Law in a series circuit
+
–
V = 230V
R3 = 6 Ω
R1 = 4 Ω
R2 = 5 Ω
Consider the diagram. Work out the current in the circuit, to one decimal place.
Hint: first find the equivalent resistance of the circuit, then rearrange Ohm’s Law to make current the subject.
Resource 3: Key mathematical electrical principles
Ohm’s Law

## Slide 13: Ohm’s law in a series circuit: Answer
+
–
V = 230V
R3 = 6 Ω
R1 = 4 Ω
R2 = 5 Ω
Consider the diagram. Work out the current in the circuit, to one decimal place.
First find the equivalent resistance:
Use Ohm’s Law to calculate the current:
Resource 3: Key mathematical electrical principles
Ohm’s Law

## Slide 14: Ohm’s Law for identifying hazards
The wrong resistance for a circuit can be dangerous.
If the resistance is too low, the resulting high current can lead to heat damage of components and even fires.
If the resistance is too high, the current may be insufficient for circuit components to operate.
Accurate calculations are essential to ensure the safety and efficiency of electrical systems.
YOU TRY
When the insulation on a wire gets damaged, its resistance might decrease.
What happens to the current?
What hazards could this create?
Resource 3: Key mathematical electrical principles
Ohm’s Law

## Slide 15: Ohm’s Law for identifying hazards
An electric cable in an industrial grinder has a resistance of 0.6 Ω and a DC supply of 100 V. Is this setup potentially hazardous?
TIP Most power tools are designed for a current of around 20 A or less.
Resource 3: Key mathematical electrical principles
Ohm’s Law
Notes: Image © Shutterstock/maroke

## Slide 16: Ohm’s Law for identifying hazards: Answer
An electric cable in an industrial grinder has a resistance of 0.6 Ω and a DC supply of 100 V. Is this setup potentially hazardous?
Rearrange Ohm’s Law, then substitute the values:
Yes, this cable is potentially hazardous
because its current is much higher than the 20 A it is designed for. It should not be used.
Resource 3: Key mathematical electrical principles
TIP Most power tools are designed for a current of around 20 A or less.
Ohm’s Law
Notes: .

## Slide 17: What is power and how is it relevant?
Power is the rate at which energy is transferred.
Power and energy both can take various forms, mechanical and electrical being the main categories.
It is essential to be able to calculate power for the design of safe and efficient electrical circuits.
Resource 3: Key mathematical electrical principles
Power
Notes: Image © Shutterstock/arturnichiporenko

## Slide 18: Calculating power
Intuitively, we know that increasing the voltage or current in a circuit increases its power.
A formula for electrical power is:
Show that this can be rearranged to:
The SI unit for power is watts (W).
Resource 3: Key mathematical electrical principles
Power

## Slide 19: Using the electrical power formula
An air conditioner has a power rating of 1500 W and is supplied by a 208 V single-phase system.
Assuming the circuit is purely resistive, calculate the current, giving your answer to two significant figures.
Key point
Current is in the opposite direction to electron flow.
We avoid referring to ‘current flow’ because it is the electrons that flow.
Resource 3: Key mathematical electrical principles
Power

## Slide 20: Using the electrical power formula: Answer
An air conditioner has a power rating of 1500 W and is supplied by a 208 V single-phase system.
Assuming the circuit is purely resistive, calculate the current, giving your answer to two significant figures.
Use the power equation to solve for current:
Key point
Current is in the opposite direction to electron flow.
We avoid referring to ‘current flow’ because it is the electrons that flow.
Resource 3: Key mathematical electrical principles
Power

## Slide 21: What is power dissipation?
Power dissipation in electrical systems is often referred to as ‘lost’ energy or power, but energy is never lost.
Instead, it is converted into different energy forms, such as heat and light due to resistance in the circuit.
Accurate calculations are key for avoiding too much heat generation resulting in damage, electrical failure or even fire.
Resource 3: Key mathematical electrical principles
Power
Notes: Image © Shutterstock/puha dorin

## Slide 22: Calculating power dissipation
Another formula for power is
Can you show this by substituting Ohm’s Law
into
?
A DC lighting circuit draws 3 A of current. The resistance of the cable supplying the lights is 0.5 Ω. Calculate the power dissipation across the cable.
Over time, the power dissipation in the circuit increases to 5 W. Calculate the new resistance across this cable to two decimal places.
Resource 3: Key mathematical electrical principles
Power

## Slide 23: Calculating power dissipation: Answer
A DC lighting circuit draws 3 A of current. The resistance of the cable supplying the lights is 0.5 Ω. Calculate the power dissipation across the cable.
Over time, the power dissipation in the circuit increases to 5 W. Calculate the new resistance across this cable to two decimal places.
Another formula for power is
Can you show this by substituting Ohm’s Law
into
?
Resource 3: Key mathematical electrical principles
Power

## Slide 24: Basics of a transformer
A transformer uses electromagnetic induction to change the voltage level of an AC current whilst keeping the frequency constant.
V = voltage, = current, = number of turns and the S and P subscripts refer to the Secondary and Primary coils.
A transformer has:
a primary coil connected to the input AC voltage
a secondary coil that delivers the transformed output voltage
an iron core.
Resource 3: Key mathematical electrical principles
Transformers
Notes: Image © Shutterstock/VectorMine

## Slide 25: Transformer formulae
A step-up transformer has more turns in the secondary coil than the primary coil, resulting in a higher voltage on the secondary.
A step-down transformer has fewer turns in the secondary than the primary coil, resulting in a lower voltage on the secondary.
Resource 3: Key mathematical electrical principles
Transformers
Notes: Image © Shutterstock/VectorMine

## Slide 26: Transformer formulae
The ratio of voltages between the two coils depends on the ratio of turns in the coils, with relationships:
V = voltage,
= current,
= number of turns
subscripts refer to Secondary and Primary coils.
Which formula relates the power of the primary and secondary coils?
Resource 3: Key mathematical electrical principles
Transformers
Notes: Image © Shutterstock/VectorMine

## Slide 27: Exam-style question 1
A house is supplied by solar panels that produce 240 V AC, but the building’s appliances operate at 400 V.
(a) Explain whether a step-up or step-down transformer is needed to connect the solar panels to the electrical system of the house.
The building requires 12 kW of power. Work out the current on the side of the transformer connected to the:
(b) solar panels
(c) house.
Resource 3: Key mathematical electrical principles
Exam-style question

## Slide 28: Exam-style question 1: Answer
It requires a step-up transformer because it must ‘step up’ the voltage from 240 V to 400 V.
A house is supplied by solar panels that produce 240 V AC, but the building’s appliances operate at 400 V.
(a) Explain whether a step-up or step-down transformer is needed to connect the solar panels to the electrical system of the house.
Resource 3: Key mathematical electrical principles
Exam-style question
Notes: Image © Shutterstock/ASyamil

## Slide 29: Exam-style question 1: Answer
A house is supplied by solar panels that produce 240 V AC, but the building’s appliances operate at 400 V.
(b) The building requires 12 kW of power. Work out the current on the side of the transformer connected to the solar panels.
First, convert 12 kW to W:
Then rearrange the power equation to solve for current:
Resource 3: Key mathematical electrical principles
Exam-style question

## Slide 30: Exam-style question 1: Answer
A house is supplied by solar panels that produce 240 V AC, but the building’s appliances operate at 400 V.
(c) The building requires 12 kW of power. Work out the current on the side of the transformer connected to the house.
First, convert 12 kW to W:
Then rearrange the power equation to solve for current:
Resource 3: Key mathematical electrical principles
Exam-style question

## Slide 31: Exam-style question 2
The diagram shows a DC electric circuit.
A voltage V1 measurement across R1 shows a reading of 24 V.
(a) Calculate the total circuit current.
(b) Find the total resistance of the circuit, and hence calculate the total circuit voltage and the individual voltages across R2 and R3.
+
–
V
R1
V1
R2
R3
V2
V3
Resource 3: Key mathematical electrical principles
Exam-style question

## Slide 32: Exam-style question 2: Answer
+
–
V
R1
V1
R2
R3
V2
V3
The diagram shows a DC electric circuit.
A voltage V1 measurement across R1 shows a reading of 24 V.
(a) Calculate the total circuit current.
Use Ohm’s Law to find the current through R1:
I1
I
This is a series circuit, so the current is the same through all paths, therefore the total current is .
Resource 3: Key mathematical electrical principles
Exam-style question

## Slide 33: Exam-style question 2: Answer
The diagram shows a DC electric circuit.
(b) Find the total resistance of the circuit, and hence calculate the total circuit voltage and the individual voltages across R2 and R3.
+
–
V
R1
V1
R2
R3
V2
V3
Resistance in series are additive:
The total voltage is given by
Resource 3: Key mathematical electrical principles
Exam-style question

## Slide 34: Exam-style question 2: Answer
The diagram shows a DC electric circuit.
(b) Find the total resistance of the circuit, and hence calculate the total circuit voltage and the individual voltages across R2 and R3.
+
–
V
R1
V1
R2
R3
V2
V3
The individual voltages are found:
Note that
Resource 3: Key mathematical electrical principles
Exam-style question

## Slide 35: Name the components
Resource 3: Key mathematical electrical principles
Name the components
Notes: Shutterstock Asset id: 2652657185

## Slide 36: Name the components: Answers
Batteries | Resistor | Capacitor | Inductor, coil
ACV source | Diode, LED | Transistor | Ground
Ammeter | Voltmeter | Fuse | Lamp, bulb
One cell | Fixed resistor | Variable resistor | Potentiometer
Resource 3: Key mathematical electrical principles
Name the components
Notes: Image © Shutterstock/Mohamad_Trend

## Slide 37: In this resource, we have:
Explained key mathematical electricity science principles and their importance
Described and recalled the rules of electrical circuits
Calculated with and recalled Ohm’s law (V = IR) for a variety of different scenarios
Completed calculations involving key formulae
Calculated problems involving electrical power and its relationship with voltage
Calculated problems involving electrical power dissipation
Described the basics of transformers
Calculated problems involving step-up and step-down transformers
General competencies:
MC4 Using rules and formulae
MC5 Processing data
MC7 Interpreting and representing with mathematical diagrams
MC8 Communicating using mathematics
Resource 3: Key mathematical electrical principles
Plenary

## Slide 38: Consolidation
Choose one of the research topics below to prepare a short presentation:
  Well-known disasters as a result of other types of electrical failure relating to the maths and principles you are studying.
Present your findings in a subsequent lesson, either in small groups or to the class.
Resource 3: Key mathematical electrical principles
Consolidation