## Slide 1: Engineering and Manufacturing
Route: Engineering and Manufacturing
Topic: Fundamentals of electronics
Resource 1: Circuits, voltage and current
Notes: Image © Shutterstock/CrizzyStudio

## Slide 2: In this resource, we will:
Introduction
Describe the key differences between parallel and series circuits
Identify standard electronic symbols and describe their function
Explain the function and uses of diodes and transistors
Use a breadboard to build an electronic circuit
General competencies:
English:
EC5 Synthesise information
Maths:
MC2 Estimating, calculating and error spotting
MC4 Using rules and formulae
Digital:
DC1 Use digital technology and media effectively
Resource 1: Circuits, voltage and current

## Slide 3: Series and parallel circuits
Resource 1: Circuits, voltage and current
Activity 1
Notes: Circuits and calculations video: https://vimeo.com/1219232696

## Slide 4: Series and parallel circuits
Activity 1
Resource 1: Circuits, voltage and current
Describe the main differences between these two circuits.
Calculate the total resistance in each circuit.
Calculate the power dissipated by each resistor combination.
Resistor | Resistance ( )
1 | 200
2 | 100
3 | 200
4 | 100

## Slide 5: Recap questions (answers)
Activity 1
Resource 1: Circuits, voltage and current
Parallel circuit:
3.
Series circuit:
= = 0.0833 W
Parallel circuit:
= = 0.375 W
2. Series circuit:
Rtotal = R1 + R2
Rtotal = 200 + 100
Rtotal = 300 Ω
1. Series – current must pass through all components
Parallel – current splits at the junction

## Slide 6: The mystery flaw
Predict: Look at the diagram. Will the LEDs light up? Why/Why not?
Observe: Build the circuit. Record what actually happens.
Explain: If the circuit failed, identify the ‘flaw’. (Hint: Check the current and the total current available.)
Activity 1
Resource 1: Circuits, voltage and current
Resources needed
R1 Activity 1 Worksheet

## Slide 7: Series and parallel circuits – summary
Activity 1
Resource 1: Circuits, voltage and current
 | Series circuit | Parallel circuit
Voltage (p.d.) | Supply p.d. divided between components Vtotal = V1 + V2 + V3 + … | Each branch in a circuit receives the supply voltage (regardless of resistance) Vsupply = V1 = V2 = V3 = …
Current | Constant at all points in circuit I1 = I2 = I3 = … | Current splits between branches Itotal = I1 + I2 + I3 + …
Resistance | Total resistance is the sum of the individual resistances Rtotal = R1 + R2 + R3 + … | Resistance in parallel is calculated using:
 | Series circuit | Parallel circuit
Voltage (p.d.) | Supply p.d. divided between components Vtotal = V1 + V2 + V3 + … | Each branch in a circuit receives the supply voltage (regardless of resistance) Vsupply = V1 = V2 = V3 = …
Current | Constant at all points in circuit I1 = I2 = I3 = … | Current splits between branches Itotal = I1 + I2 + I3 + …
Resistance | Total resistance is the sum of the individual resistances Rtotal = R1 + R2 + R3 + … | Resistance in parallel is calculated using:

## Slide 8: Standard symbols (BS EN 60617)
Activity 1
Resource 1: Circuits, voltage and current

## Slide 9: Standard symbols (BS EN 60617)
Activity 1
Resource 1: Circuits, voltage and current

## Slide 10: Transistors
A transistor is a semiconductor device used to switch electronic signals or amplify them.
Examples of use: computer memory chips, mobile phones and car engine management systems.
Activity 2
Resource 1: Circuits, voltage and current
Notes: Image (left) © Shutterstock/udaya fire
Image (right) © Shutterstock/Sergiy Kuzmin

## Slide 11: BC547 NPN transistor – The electronic gate
Its function is as an electronic switch or a signal amplifier in electronic circuits, allowing a small electrical signal to control a much larger current.
Collector (C): Where the ‘large’ current waits.
Base (B): The ‘gate’ or trigger.
Emitter (E): Where the current exits to Ground (0"V").
Activity 2
Resource 1: Circuits, voltage and current

## Slide 12: BC547 NPN transistor – 0.7 rule
The BC547 acts like an electrically operated switch with no moving parts.
A small current applied to the Base pin allows a larger current to flow between the Collector and Emitter pins. The ‘gate’ only opens when the Base reaches 0.7 "V". Anything less, and the circuit stays ‘Cut-off’ (OFF).
Activity 2
Resource 1: Circuits, voltage and current

## Slide 13: Diodes
A diode is an electronic component that allows current to flow in one direction while blocking it in the opposite direction.
Examples of use: AC to DC rectifier, lighting (LEDs)
Activity 2
Resource 1: Circuits, voltage and current
Positive (anode)
Negative (cathode)
Positive (anode)
Negative (cathode)
Notes: Image (left) © Shutterstock/infinetsoft
Image (right) © Shutterstock/Romashko Yuliia

## Slide 14: Breadboards
Activity 2
Resource 1: Circuits, voltage and current

## Slide 15: How the breadboard ‘thinks’
Power Rails (Horizontal): Linked all the way across. Used for +𝑉_𝑐𝑐and Ground.
Terminal Strips (Vertical): Linked in groups of 5.
The ‘Trench’: The middle gap separates the two sides.
Red Flag: Never plug both ends of a component into the same vertical column, this creates a short circuit.
Activity 2
Resource 1: Circuits, voltage and current

## Slide 16: Transistor circuit
Build the following circuit on your breadboard.
What voltage do you measure at the base of each transistor when its LED is on vs off?
Can you measure how long one LED stays on?
What happens to the voltage at the base just before switching?
Activity 2
Resource 1: Circuits, voltage and current

## Slide 17: Supply and Forward Voltage
Supply Voltage (V-'supply' ): The total voltage provided by the power source (e.g., a 9V battery or 5V rail).
Forward Voltage (V-'forward' or V-f): The fixed voltage drop needed across an LED so it can turn on (typically ∼1.8 'V'-2.2 'V' for red LEDs).
Now turn to your activity book to complete the worked examples.
Activity 2
Resource 1: Circuits, voltage and current

## Slide 18: Worked example – Voltage drop
Activity 2
Resources needed
R1 Activity 2 Worksheet
R1 Activity 2 Worksheet answers
Resource 1: Circuits, voltage and current
Q1: You have a 9 V battery and want to power two red LEDs in a single series string. Each LED has a forward voltage (𝑉forward) of 2.2 V. Explain whether the LEDS will light.
The total forward voltage of the LEDs is:
2.2 V + 2.2 V = 4.4 V.
The 9 V battery is sufficient because:
9 V > 4.4.
So, the LEDs will light because the total forward voltage (4.4 V) is less than the supply voltage (9 V).
Note: The remaining 4.6 V should be dropped across a resistor to limit the current and prevent the LEDs from burning out.

## Slide 19: Worked example – Voltage drop
Activity 2
Resources needed
R1 Activity 2 Worksheet
R1 Activity 2 Worksheet answers
Resource 1: Circuits, voltage and current
Q2: An LED has a forward voltage of 2 V and is connected to a 9 V power supply. The LED should operate at a current of 20 mA (0.02 A).
Calculate the value of the series resistor required to protect the LED.
Step 1: Substitute the known values into the equation. Step 2: Calculate the resistor value.
(Use a 470 Ω standard resistor for a safety margin.)

## Slide 20: Worked example – Transistor gain
Activity 2
Resources needed
R1 Activity 2 Worksheet
R1 Activity 2 Worksheet answers
Resource 1: Circuits, voltage and current
Q3: You measure a base current (𝐼B) of 0.005 A (5mA) and a collector current (𝐼C) of 0.15 A (150mA). Calculate the gain.
Step 1: Use the formula:
Step 2: Substitute the known values and calculate the gain:
Context: This means the collector current is 300 times the base current. This is a typical gain value for a BC547 transistor.

## Slide 21: In this resource, we have:
Plenary
Described the key differences between parallel and series circuits
Identified standard electronic symbols and described their function
Explained the function and uses of diodes and transistors
Used a breadboard to build an electronic circuit
General competencies:
English:
EC5 Synthesise information
Maths:
MC2 Estimating, calculating and error spotting
MC4 Using rules and formulae
Digital:
DC1 Use digital technology and media effectively
Resource 1: Circuits, voltage and current