## Slide 1: Building Services Engineering
Topic: Practical mathematics
Route: Construction
Resource 4: Key mathematical heat principles
Notes: Image © Shutterstock/Gorodenkoff

## Slide 2: Key mathematical heat principles: glazing company
Resource 4: Key mathematical heat principles
Video
Notes: Key mathematical heat principles: glazing company video: https://vimeo.com/1206421925/83af139629

## Slide 3: In this resource, we will:
Complete calculations involving mechanical power
Describe and use the principles of heat transfer
Explain what specific heat capacity (SHC or c) is and use the formula
  energy = mcΔT
Calculate the heat loss in buildings based on the thermal conductivity of common materials used to construct the building fabric, changes of air and ventilation
Calculate heat loss using:
  U values for walls, roof, windows, doors, floors, air changes
  Q = UA (T1 − T2).
General competencies:
MC4 Using rules and formulae
MC5 Processing data
MC7 Interpreting and representing with mathematical diagrams
MC8 Communicating using mathematics
Resource 4: Key mathematical heat principles
Introduction

## Slide 4: Heat in construction
Understanding heat is important to construction and building design.
Chemical reactions in concrete generate heat (exothermic). If it gets too hot, it cracks. Civil engineers manage the pour.
Solar gains from windows can cause a building to heat up and must be mitigating with shading and ventilation.
Resource 4: Key mathematical heat principles
Heat transfer overview
Notes: Image © Shutterstock/Stepan Skorobogadko

## Slide 5: Types of heat transfer
Conduction
  Example: cold bridging through steel beams
Convection
  Example: radiator circulation
Radiation
  Example: gain through glazing
These may occur at the same time.
Can you identify the types of heat transfer in the thermal image?
Resource 4: Key mathematical heat principles
Heat transfer overview
Notes: Image © Shutterstock/Ivan Smuk

## Slide 6: Applications of heat formulae
Heat calculations are used to:
design heating and ventilation systems;
select the most suitable types and thicknesses of insulation materials (such as fiberglass, mineral wool, rigid foam);
consider energy efficiency and comply with regulations;
create a comfortable living or working space.
Resource 4: Key mathematical heat principles
Heat transfer overview
Notes: Image © Shutterstock/Juice Verve

## Slide 7: Properties of materials
An important consideration in construction is how to keep a building within a desired temperature range.
We need to work out which materials would be the most useful for the context.
We need to understand properties of materials that are used in the relevant heat calculation formulae.
When choosing materials, compromises need to be made. A very lightweight but fragile material might be the best insulator or conductor, but not useful for load bearing, or it might be too expensive.
Material properties quantify these ideas.
Compromise
Resource 4: Key mathematical heat principles
Heat transfer overview

## Slide 8: Specific heat capacity
Specific heat capacity (SHC), with symbol c, is a property that measures how much heat energy a substance needs to change its temperature.
Specifically, it is the amount of heat energy required to raise the temperature of 1 kilogram of a substance by 1 degree Kelvin.
Its units are joules per kilogram Kelvin (J/kgK)
You may also see J/kgºC.
Each material has its own specific heat capacity.
Which is a better insulator?
Resource 4: Key mathematical heat principles
Specific heat capacity

## Slide 9: The energy formula using SHC (c)
Specific heat capacity relates heat energy to mass and temperature change:
You can rearrange this equation to solve for any of the other quantities.
You might see E for energy used in place of Q, which is a more general formula.
is the heat energy measured in J
is mass in kg
is specific heat capacity in J/kgK
is the temperature difference in K or ºC.
The variables
Resource 4: Key mathematical heat principles
Specific heat capacity

## Slide 10: Using specific heat capacity
A concrete floor has a mass of 920 kg and a specific heat capacity of 300 J/kgK.
If the floor absorbs 700 kJ of heat per square metre, by how much will its temperature rise?
Hint
Make sure that your variables are in SI units for your calculations.
Resource 4: Key mathematical heat principles
Specific heat capacity

## Slide 11: Using specific heat capacity: Answer
A concrete floor has a mass of 920 kg and a specific heat capacity of 300 J/kgK.
If the floor absorbs 700 kJ of heat per square metre, by how much will its temperature rise?
Convert to SI units:
Rearrange the formula and substitute:
Hint
Make sure that your variables are in SI units for your calculations.
Resource 4: Key mathematical heat principles
Specific heat capacity

## Slide 12: Thermal resistance
Thermal resistance, is a measure of how strongly a single material resists heat flow.
is the sum of all the individualvalues for each component of the assembly:
An assembly is a combination of materials, such as found in a wall, door or floor.
Can you identify how adding external wall insulation helps resist heat flow?
Resource 4: Key mathematical heat principles
Thermal resistance and conductivity
Adhesive
External Wall
Insulation Material
Finishing Coat
Primer Coat
Reinforcing Mesh
Fixing Anchor
Notes: Image © Shutterstock/Radzas2008

## Slide 13: The formula for thermal resistance
The formula for thermal resistance is
The formula for the total thermal resistance is the same but with total and effective quantities:
r is the thermal resistance in m2K/W
t is the thickness in m
k is the thermal conductivity in W/mK
Note the between m and K where m means unit metres not prefix milli.
The variables
Resource 4: Key mathematical heat principles
Thermal resistance and conductivity

## Slide 14: The coefficient of thermal conductivity
The coefficient of thermal conductivity, , is a measure of how easily a material conducts heat.
It measures how easily heat flows through a material dependent on the material’s conductivity.
The units of are watts per metre Kelvin: W/mK.
-values are used in the formulae:
The intrinsic ability to store heat is decided by its molecular structure.
Site tip k-values are found on the manufacturer's datasheet. You need these sheets to prove to the Building Inspector that the wall meets regulations.
Resource 4: Key mathematical heat principles
Thermal resistance and conductivity

## Slide 15: Using the thermal resistance formula
A wall in a school has a 60 mm layer of insulation with a thermal conductivity (-value) of 0.056 W/mK.
Calculate the thermal resistance of the layer.
Resource 4: Key mathematical heat principles
Thermal resistance and conductivity

## Slide 16: Using the thermal resistance formula: Answer
A wall in a school has a 60 mm layer of insulation with a thermal conductivity (-value) of 0.056 W/mK.
Calculate the thermal resistance of the layer.
Convert 60 mm to m:
Substitute thickness and -value into formula:
(4 s.f.)
Note
Increasing the thickness of insulation increases thermal resistance, meaning that the heat flows more slowly through the wall.
Try the calculation again with a larger .
Resource 4: Key mathematical heat principles
Thermal resistance and conductivity

## Slide 17: Overall heat transfer coefficient
The overall heat transfer coefficient,is a measure of how easily heat flows through an assembly.
It is the reciprocal of , the total thermal resistance.
The units of U are:
watts per square-metre-kelvin W/m2 K.
Remember that reciprocal of means 1 over, which is also known as the inverse.
Resource 4: Key mathematical heat principles
Overall heat transfer coefficient and U-values

## Slide 18: The heat loss formula
The formula for heat loss is:
Q shows how fast a building is losing or gaining heat through its walls, roof or windows, as is directly proportional to U.
Q is the rate of heat (energy) loss in W
U is the overall heat transfer coefficient in W/m2K
A is area in m2
T₁ −T₂ (or ) is the temperature difference in K or ºC.
The variables
Resource 4: Key mathematical heat principles
Overall heat transfer coefficient and U-values

## Slide 19: The heat loss formula
Q is the rate of heat (energy) loss in W
U is the overall heat transfer coefficient in W/m2K
A is area in m2
T₁ −T₂ (or ) is the temperature difference in K or ºC.
The variables
The formula for heat loss is:
U-value is the rate of heat loss through building element.
lower U-value = better insulated less energy wasted = lower heating costs
Resource 4: Key mathematical heat principles
Overall heat transfer coefficient and U-values

## Slide 20: Example using the heat loss formula
A server room has a flat roof of area 150 m2 that has a U-value of U = 0.2 W/m2K.
The indoor temperature is set to 28°C. Calculate the rate of heat loss through the roof when the external temperature is 17°C.
Resource 4: Key mathematical heat principles
Overall heat transfer coefficient and U-values

## Slide 21: Example using the heat loss formula: Answer
A single server generates around 300 W of heat, so, a roomful would generate thousands of watts, which is more than can escape through the roof.
If the cooling system fails in a server room, equipment overheats.
We calculate heat gain to size the Air Conditioning (AC) units.
A server room has a flat roof of area 150 m2 that has a U-value of U = 0.2 W/m2K.
The indoor temperature is set to 28°C. Calculate the rate of heat loss through the roof when the external temperature is 17°C.
Substitute the values into the formula:
Resource 4: Key mathematical heat principles
Overall heat transfer coefficient and U-values

## Slide 22: Power and heat
Power is the rate at which heat energy is transferred:
For example, a 2000 W kettle transfers 2000 J of heat energy per second to heat the water.
How much energy does it transfer in 30 seconds?
Energy is heat transferred and measured in joules (J).
Time is measured in seconds (s).
Power is the rate heat is transferred, measured in watts (W).
The variables
Resource 4: Key mathematical heat principles
Power

## Slide 23: In this resource, we have:
Completed calculations involving mechanical power
Described and used the principles of heat transfer
Explained what specific heat capacity (SHC or c) is and used the formula
  energy = mcΔT
Calculated the heat loss in buildings based on the thermal conductivity of common materials used to construct the building fabric, changes of air and ventilation
Calculated heat loss using:
  U values for walls, roof, windows, doors, floors, air changes
  Q = UA (T1 − T2).
General competencies:
MC4 Using rules and formulae
MC5 Processing data
MC7 Interpreting and representing with mathematical diagrams
MC8 Communicating using mathematics
Resource 4: Key mathematical heat principles
Plenary

## Slide 24: Consolidation
Choose one of the research topics below to prepare a short presentation:
  the science and maths behind vacuum glazing compared to the more commonly used types of double glazing that use gases, and single glazing
  the pros and cons of heat pumps.
Present your findings in a subsequent lesson, either in small groups or to the class.
For the latter topic, think about whether you think heat pumps are a good idea or not for a traditional debate.
Consolidation
Resource 4: Key mathematical heat principles