## Slide 1: Building Services Engineering
Topic: Practical mathematics
Route: Construction
Resource 2: Key mathematical mechanics principles
Notes: Image © Shutterstock/Gorodenkoff

## Slide 2: Key mathematical mechanics principles: structural engineer
Resource 2: Key mathematical mechanics principles
Video
Notes: Key mathematical mechanics principles: structural engineer video: https://vimeo.com/1198454546/2632cafae6

## Slide 3: In this resource, we will:
Explain the effects of gravity in terms of acceleration
Explain the relationship between energy and power in terms of time
Describe how efficiency changes input and output power values including typical losses associated with efficiency
Describe the relationship between acceleration, force, work, energy, power, and work done
Explain the basic principles of levers, pulleys and moments
Complete calculations involving key formulae
General competencies:
MC4 Using rules and formulae
MC5 Processing data
MC7 Interpreting and representing with mathematical diagrams
MC8 Communicating using mathematics
Resource 2: Key mathematical mechanics principles
Introduction

## Slide 4: Gravitational freefall and mass
In the absence of air resistance, all objects fall at the same rate regardless of mass.
This idea is often instinctively rejected, but it is easy to prove.
The confusion arises because objects in air experience air resistance or drag, which acts in the opposite direction to their motion.
Resource 2: Key mathematical mechanics principles
Forces
Notes: Image © Shutterstock/Collection Maykova

## Slide 5: Acceleration due to gravity
Gravity causes objects to accelerate independently of their mass. On Earth, the gravitational acceleration is approximately 9.8 m/s2.
This means that the velocity of a falling object increases by about 9.8 m/s every second, as long as no other forces (like air resistance) are acting on it.
Objects with mass attract each other, and how strong the attraction, depends on the mass of both objects. Because the Earth is so massive compared to most objects, only the mass of the Earth matters in calculations on Earth, so the attraction between them is considered constant: 9.8 m/s2.
TIP
If anyone attempts to argue this principle with you by dropping a piece of paper with another object, crumple the paper into a tight ball and repeat the experiment, or use a large block of printer paper!
Resource 2: Key mathematical mechanics principles
Forces

## Slide 6: Key formulae for mechanical science principles
Here are the key formulae that you will need for this topic, along with their symbols and SI units:
force,
work (energy),
power,
Resource 2: Key mathematical mechanics principles
Forces

## Slide 7: Thinking in forces
Think of examples of each type of force.
  Tension: Pulling forces that stretch materials
  Compression: Pushing forces that compact materials
  Bending: Combined tension and compression creating curvature
  Torsion: Twisting forces causing rotational stress
Resource 2: Key mathematical mechanics principles
Forces

## Slide 8: Thinking in forces: Answers
Think of examples of each type of force.
  Tension: Pulling forces that stretch materials
  Wires stretched between pylons
  Compression: Pushing forces that compact materials
  The weight of a building on concrete pillars
  Bending: Combined tension and compression creating curvature
  A shelf bending under the weight of books
  Torsion: Twisting forces causing rotational stress
  The twisting on a drive shaft
Resource 2: Key mathematical mechanics principles
Forces

## Slide 9: What is a force?
A force is a push or a pull that can cause an object to start to move, speed up, slow down or change its direction or shape.
The mechanics formula is:
Forces come in different forms: weight, effort, thrust, friction, resistance, normal reaction, drag, tension.
Mass is measured in kilograms (kg).
Acceleration is measured in metres per second squared, or metres per second per second (m/s2).
Force is measured in newtons ().
The variables
Resource 2: Key mathematical mechanics principles
Forces

## Slide 10: Calculating force
A carpenter needs to use 20 wooden joists. She knows that one joist has a mass of 1.6 kg. Calculate the weight of the 20 joists.
Remember that mass is not weight. Weight is a force due to the effect of gravity on a mass.
You will usually be told to use
Resource 2: Key mathematical mechanics principles
Forces

## Slide 11: Calculating force: Answer
A carpenter needs to use 20 wooden joists. She knows that one joist has a mass of 1.6 kg. Calculate the weight of the 20 joists.
The mass of 20 joists is:
Use with
Remember that mass is not weight. Weight is a force due to the effect of gravity on a mass.
You will usually be told to use
Resource 2: Key mathematical mechanics principles
Forces

## Slide 12: How materials respond to force
Stress describes how force is distributed inside a material:
measured in pascals (Pa) or N/m2.
Strain describes how much a material deforms relative to its original size:
which is a ratio, so it has no units.
Stress–strain relationships describe how materials respond to forces.
Mini task
Which material has a higher strain under the same load: Rubber or concrete?
Resource 2: Key mathematical mechanics principles
Forces

## Slide 13: Energy and work done
What is energy?
Energy is the ability to cause change.
Example: energy is stored in a battery. It has potential to create a current in a wire.
What is work?
Work is transferring energy by applying a force over a distance. In mechanics:
Work done (energy) is measured in joules (J).
Power is measured in watts (W).
Time is measured in seconds (s).
If you are given hours or minutes in a question, remember to convert to seconds!
The variables
Resource 2: Key mathematical mechanics principles
Energy and work done

## Slide 14: Calculating work done
A construction worker pushes a pallet truck a distance of .
He applies a constant horizontal force of to keep the truck moving.
Give your answer in joules.
Resource 2: Key mathematical mechanics principles
Energy and work done
Notes: Image © Shutterstock/Microgen

## Slide 15: Calculating work done: Answer
A construction worker pushes a pallet truck a distance of .
He applies a constant horizontal force of to keep the truck moving.
Give your answer in joules.
First convert centimetres to metres:
Use
EXAM TIP
Always show your reasoning clearly. You can never write down too much information, and sometimes just writing a formula will get you marks.
Resource 2: Key mathematical mechanics principles
Energy and work done

## Slide 16: Simple pulley
A simple pulley has one wheel and a rope to help lift heavy loads.
It does not reduce the effort but changes the direction of the effort, which can make lifting easier.
The formula for work done lifting an object with mass to height is:
In this formula is the force of gravity on the load.
wheel
rope
effort
load
Resource 2: Key mathematical mechanics principles
Energy and work done

## Slide 17: Pulleys that reduce effort
Pulleys can be designed reduce effort.
This pulley reduces the force required by half because there are two rope segments pulling on the load.
The user will need to pull the rope twice as far, so the same work is done over a longer distance, which reduces the force required.
fixed wheel
rope
effort
free wheel
load
½ load
Resource 2: Key mathematical mechanics principles
Energy and work done

## Slide 18: Levers as a tool
More than 2000 years ago, the Greek philosopher Archimedes said:
"Give me a place to stand and a lever long enough, and I will move the world."
What do you think he meant by this?
Resource 2: Key mathematical mechanics principles
Moments and torque
Notes: Image © Shutterstock/Pat Marais

## Slide 19: Some history of levers
Whilst Archimedes was the first person known to write about levers, simple levers such as sticks and oars were used many years before he was born.
Levers were used in ancient Egypt and Mesopotamia to lift water and large stone structures known as obelisks.
They were also used to position the standing stones to create Stonehenge.
Resource 2: Key mathematical mechanics principles
Moments and torque
Notes: Image © Shutterstock/Second Saturn

## Slide 20: Moments and torque
A moment is the effect of a force at a distance that tends to cause a rotation about a pivot point, such as with beams or levers.
Torque is conceptually the same as a moment, but more often used in dynamic contexts such as in engines or wheels.
Force is measured in newtons (N).
Distance is measured in metres, perpendicular from the pivot (m).
Moment measures the turning force in the direction of the force and is measured in newton-metres (Nm).
1 Nm = 1 J if work is done.
The variables
Resource 2: Key mathematical mechanics principles
Moments and torque

## Slide 21: How does a lever work?
Levers provide a mechanical advantage by doing work over a longer distance.
Class 1: fulcrum located between effort and load.
Class 2: load located between fulcrum and effort.
Class 3: effort located between fulcrum and load.
There are three categories of lever:
effort (input force)
load
(opposing force)
fulcrum
rigid bar (beam)
Resource 2: Key mathematical mechanics principles
Moments and torque

## Slide 22: Three classes of lever
Exercise
When each of these tools is being used, identify the typical positions of the fulcrum, effort and load, and thus the class of lever.
Resource 2: Key mathematical mechanics principles
Moments and torque
Notes: Image (left) (c) Shutterstock/Anton Starikov
Image (centre) (c) Shutterstock/Pedal to the Stock
Image (right) (c) Shutterstock/Passakorn sakulphan

## Slide 23: Three classes of lever
load
(object)
effort
fulcrum
fulcrum
effort
load
(contents)
fulcrum
effort (fingers)
load
(object)
Exercise
Can you give another example of each class of lever?
Resource 2: Key mathematical mechanics principles
Moments and torque
Notes: Image (left) (c) Shutterstock/Anton Starikov
Image (centre) (c) Shutterstock/Pedal to the Stock
Image (right) (c) Shutterstock/Passakorn sakulphan

## Slide 24: The theory of moments
When a lever is in equilibrium (not rotating):
The clockwise moment equals the anti-clockwise moment,
FE is the effort force a is the perpendicular distance of FE from the fulcrum
FL is the load force b is the perpendicular distance of FL from the fulcrum.
a
b
a
b
a
b
Resource 2: Key mathematical mechanics principles
Moments and torque

## Slide 25: Calculating moments
A plank is balanced on a fulcrum with a 50 N load placed 0.8 m from the fulcrum. An effort 1.4 m from the fulcrum is applied on the other side. Would an effort of 30 N be enough to lift the load?
50 N
1.4 m
0.8 m
Resource 2: Key mathematical mechanics principles
Moments and torque

## Slide 26: Calculating moments: Answer
A plank is balanced on a fulcrum with a 50 N load placed 0.8 m from the fulcrum. An effort 1.4 m from the fulcrum is applied on the other side. Would an effort of 30 N be enough to lift the load?
clockwise
Since , the effort is
enough to lift the load.
50 N
1.4 m
0.8 m
Resource 2: Key mathematical mechanics principles
Moments and torque

## Slide 27: What is power?
Power is the rate at which energy is used or transferred, that is, how quickly.
So power is energy per unit time:
Energy is measured in joules (J).
Power is measured in watts (W) .
Time is measured in seconds (s).
If you are given hours or minutes in a question, remember to convert to seconds!
The variables
SITE TIP
We calculate power to size our generators. Running a 12-kW concrete breaker will trip the supply of a 10-kW generator and stop work.
Resource 2: Key mathematical mechanics principles
Power

## Slide 28: Calculating power
The worker in the previous question pushes the pallet truck the required distance in exactly 5 seconds. How much power, to the nearest integer, is required to move the pallet truck?
Data from the previous question:
force = 230 N
distance = 5.3 m
work done = 1219 J
Work done is the energy in the formula for this problem.
Resource 2: Key mathematical mechanics principles
Power

## Slide 29: Calculating power: Answer
The worker in the previous question pushes the pallet truck the required distance in exactly 5 seconds. How much power, to the nearest integer, is required to move the pallet truck?
Data from the previous question:
force = 230 N
distance = 5.3 m
work done = 1219 J
Work done is the energy in the formula for this problem.
Resource 2: Key mathematical mechanics principles
Power

## Slide 30: Calculating hoist motor efficiency
Old motor
input: 10 kW
output: 7.5 kW
Modern motor
input:10 kW
output: 9.2 kW
Using the data provided, how much more efficient is the modern motor than old electric motor? (Part L compliance)
Resource 2: Key mathematical mechanics principles
Power

## Slide 31: Calculating hoist motor efficiency: Answer
Using the data provided, how much more efficient is the modern motor than old electric motor? (Part L compliance)
So, the new motor is more efficient.
Resource 2: Key mathematical mechanics principles
Power
Old motor
input: 10 kW
output: 7.5 kW
Modern motor
input:10 kW
output: 9.2 kW

## Slide 32: In this resource, we have:
Explained the effects of gravity in terms of acceleration
Explained the relationship between energy and power in terms of time
Described how efficiency changes input and output power values including typical losses associated with efficiency
Described the relationship between acceleration, force, work, energy, power, and work done
Explained the basic principles of levers, pulleys and moments
Completed calculations involving key formulae
General competencies:
MC4 Using rules and formulae
MC5 Processing data
MC7 Interpreting and representing with mathematical diagrams
MC8 Communicating using mathematics
Resource 2: Key mathematical mechanics principles
Plenary

## Slide 33: Consolidation
Choose one of the research topics below to prepare a short presentation:
  The mechanical principles behind reinforcing of the Millennium Bridge in London, due to excessive lateral sway.
  Disasters related to inaccurate load calculations as a result of inaccurate calculations.
Present your findings in a subsequent lesson, either in small groups or to the class.
Consolidation
Resource 2: Key mathematical mechanics principles